## Slide 1: Internet Explained
Software University
https://softuni.bg
SoftUni Team
Technical Trainers

## Slide 2: Table of Contents
Introduction to Internet
How does the Internet work?
Sending and Receiving Information
Internet Protocol
Reliability and TCP
The OSI Model
Network Hardware
The Future of the Internet

## Slide 3: Have a Question?
sli.do
#java-web

## Slide 4: Introduction
An Introduction to the Internet

## Slide 5: Internet – History
Begins with the development of electronic computers in the 1950s.
Packet switching networks were developed in the late 1960
The internet protocol was developed in the 1970s
In the 1980s at CERN Tim Berners-Lee created the World Wide Web – the first website, linking hypertext documents into an information system, accessible from any node on the network

## Slide 6: Internet – Introduction
So, what is the Internet?
  A simple answer to that question is a wire. A wire, which is buried into the ground or even in the ocean
  That wire can be fiber optics, copper or occasionally beamed to satellites or through cell phone network

## Slide 7: Internet – Introduction (2)
ISPs (Internet Service Providers) have access to such cables
We get indirectly connected to them though ISPs
The Internet is a network of networks. It connects billions of devices together all over the globe that are connected to this wire in one form or another

## Slide 8: What is a Network?
Network - a group of two or more devices that can communicate
It is comprised of a number of different computer systems connected by physical and/or wireless connections
The scale can range from a single PC sharing out basic peripherals to massive data centers located around the World, to the Internet itself

## Slide 9: Networks and Internet
  The internet is made of hundreds of thousands of networks and billions of computers and devices connected physically
  These different systems connect to each other, communicate with each other and work together because of standards for how data is sent

## Slide 10: How Does the Internet Work?

## Slide 11: Web Server Work Model
Request
Response
Web Server
Web Resources
HTML, PDF, JPG…
Web Client
Technology
Database

## Slide 12: Important Definitions
  To understand how the Internet works, first we need to get acquainted with a few definitions
  What is?
    Server and Client
    Network Protocol
    Packets
    TCP vs UDP

## Slide 13: Servers and Clients
  All of the machines on the Internet are either servers or clients
  Servers are the machines that provide services to other machines
  Clients are the machines that are used to connect to those services

## Slide 14: Network Protocol
  Network Protocol – a set of rules and standards, that allow communication between network devices
  Network protocols include mechanisms for devices to identify and make connections with each other
  Example for standard network protocols:
    TCP, UDP, IP, ARP
    HTTP, FTP, TFTP, SMPT, SSH

## Slide 15: Packets
Sending and Receiving Information

## Slide 16: Packets
Everything that is created on a computer is translated into digital information using bits
Bits need to have a way to be transmitted over the internet
Every message, file or stream of information is broken down into small chunks called packets
When packets are sent on the internet, they usually travel the network together
But they might have to take a different route to get to the destination

## Slide 17: Packets (2)
Each packet contains some important information inside of it called the header:
  Where it came from
  Where is it going
  How long it is
    This is how the packet is known to be complete
    All the packets in the message are the same size
  How many packets there are in the overall message

## Slide 18: Traveling On the Packets in the Network

## Slide 19: Internet Protocol
216.58.214.46
www.google.com
IPv4, IPv6 and DNS

## Slide 20: Internet Protocol
  One of the most important protocols used in Internet communication is the Internet Protocol (IP)
  All the devices on the Internet have addresses
  They are called IP Addresses
  The IP address is unique to each computer or a device at the edge of the network
192.168.0.1
192.168.10.5
IP Address:
IP Address:

## Slide 21: IP Address
  An IP Address has many parts, organized in a hierarchy
  This version of IP Addressing is called IPv4
    Provides more than 4 billion 32 bits unique addresses
192.168.14.120
Subnetworks
Device address

## Slide 22: IP address classes

## Slide 23: IPv4 Private Address Space and Filtering
CIDR | IP address range | Class
10.0. 0.0/8 | 10.0. 0.0 – 10.255. 255.255 | A
172.16. 0.0/12 | 172.16. 0.0 – 172.31. 255.255 | B
192.168. 0.0/16 | 192.168. 0.0 – 192.168. 255.255 | C

## Slide 24: IPv4
  IPv4 is a sequence of four, three-digit numbers separated by a period
    Each number can be a number from 0 to 255
    IPv4 is not enough for all network devices connected to the internet
  In 1995, a new version of the internet protocol was created, it's called IPv6

## Slide 25: What Is CIDR (Classless Inter-Domain Routing)
Classless Inter-Domain Routing, is an IP addressing scheme that improves the allocation of IP addresses.
It replaces the old system based on classes A, B, and C.
This scheme also helped greatly extend the life of IPv4 as well as slow the growth of routing tables

## Slide 26: IPv6
  IPV6 uses 128 bits - 340 undecillion unique addresses
    That's more than the atoms on the surface of the Earth
  These 128 bits are organized into eight 16 bit sections
  Each 16 bit block is converted to hexadecimal and it's separated with a colon
  This is a full IPV6 address:
    3FFE:F200:0234:AB00:0123:4567:8901:ABCD
  The leading zeros in IPv6 can usually be left out

## Slide 27: What is a DNS?
  The domain name is a human way to access IP addresses for devices and websites around the world
  It is a sequence of phrases that map to a giant Internet-wide database of IP addresses
  When a domain name is entered in the browser, a request is made to something called a DNS (Domain Name Server)
  This server holds a cache of tons of domain names, and their matching IP addresses
www.softuni.bg
Domain name

## Slide 28: DNS Example
https://softuni.bg
request
response
(217.174.159.195)
IP Address | Domains
216.58.214.46 | Google.com
217.174.159.195 | Softuni.bg

## Slide 29: Reliability and TCP
TCP

## Slide 30: Reliability
When packets are transmitted from one location to another, they can take different paths
When they get to the destination, they are unorganized and sometimes not complete
So the message needs to be audited and reviewed in order to put it together in the right way
The Transmission Control Protocol or TCP does exactly that

## Slide 31: Transmission Control Protocol -TCP (1)
TCP uses a process, where it looks at all the packets in a message and checks them
Using the header information in each packet it knows:
  How many there are
  How large they should be
  In which order the packets should be in
Using this checklist, it is able to rearrange the packets

## Slide 32: Transmission Control Protocol – TCP (2)
If it finds that a packet doesn't match the expected characteristic, it is discarded
TCP has to verify that all the packets are:
  In the right order
  Free of any issues
After that it certifies the data and the packets are merged together to recreate the original file that was on the sender's device

## Slide 33: Transmission Control Protocol – TCP (3)

## Slide 34: TCP vs UDP
  TCP places reliability in a higher priority than speed or latency
  For instances where reliability isn't as important, but speed is, there is another protocol called UDP or User Datagram Protocol
  UDP doesn't do excessive reliability checks, but it can send information at a faster rate
  TCP is the foundation of how a majority of data is transmitted over networks

## Slide 35: User Datagram Protocol
  UDP does not establish a session and it does not guarantee data delivery
  It is known as the "fire-and-forget" protocol
    It sends data and it doesn't really care if the data is received at the other end
Missing packets..
I don't care..
UDP

## Slide 36: The OSI Model

## Slide 37: What is the OSI Model?
OSI model stands for Open System Interconnect
It consists of 7 layers
  Each layer serves the layer above it and in return, is served by the layer below it
Understanding each layer of the model helps us with:
  Troubleshooting
  Communicating better with technical and non-technical individuals about any system

## Slide 38: OSI Layers
OSI Model consists of 7 layers:
Example Protocols
HTTP, DNS, FTP, SMTP
TLS, SSL, compression
NetBIOS, PPTP, Sockets
TCP, UDP
IP, IPsec
ATM, Ethernet, MAC, LLC
USB, Bluetooth, 802.11a/b/g/n

## Slide 39: TCP/IP model mapping to OSI

## Slide 40: Application Layer – 7
Enables different applications like the browser to use the network and present it to the End User
Protocol examples:
  Domain Name System (DNS)
  File Transfer Protocol (FTP)
  HyperText Transfer Protocol (HTTP)
  Simple Mail Transfer Protocol (SMTP)

## Slide 41: Presentation Layer – 6
This layer is a part of an operating system (OS)
Converts incoming and outgoing data from one presentation format to another
  Example:
    From clear text to encrypted (or compressed) text
    Back to clear text

## Slide 42: Session Layer – 5
This layer sets up coordinates and terminates conversations
Its services include authentication and reconnection after an interruption
e.g.: Sockets

## Slide 43: Transport Layer – 4
Responsible for end-to-end communication over a network
Provides logical communication between application processes
Responsible for the management of error correction, providing quality and reliability to the end user
Protocol examples:
  Transmission Control Protocol (TCP)
  User Datagram Protocol (UDP)

## Slide 44: Network Layer – 3
Provides the functional and procedural means of transferring packets from one node to another
Responds to service requests from the transport layer and issues service requests to the data link layer
Protocol examples:
  Internet Protocol (IP)
  IPSec (IP + Auth)

## Slide 45: Data Link Layer – 2
Provides node-to-node data transfer
It detects and possibly corrects errors that may occur in the physical layer
Divides into two sublayers
  Medium access control (MAC) layer - controlling how devices in a network gain access to a medium and permission to transmit data
  Logical link control (LLC) layer – identifying and encapsulating network layer protocols, controls error checking and frame synchronization

## Slide 46: Data Link Layer (2) – 2
Protocol examples:
  Asynchronous Transfer Mode (ATM)
  Ethernet
  MAC

## Slide 47: Physical Layer – 1
The things you can actually physically touch
Converts the binary from the upper layers into signals, transmits them over local media (electrical, light, or radio signals)
Examples:
  Ethernet
  USB
  Bluetooth
  802.11a/b/g/n

## Slide 48: Network Hardware
Basic Hardware Components

## Slide 49: Network Hardware
Basic Hardware Components
  Cables
  Routers
  Repeaters, Hubs and Switches
  Bridges
  Gateways
  Network Interface Cards

## Slide 50: Cables and Routers
Network Cables – the transmission media to transfer data from one device to another
Router – connecting device that transfers data packets between different computer networks (operates on level 3 of OSI)

## Slide 51: Repeaters, Hubs and Switches
Repeaters, hubs and switches connect network devices together so that they can function as a single segment
  Repeater – receives a signal and regenerates it before re-transmitting, so that it can travel longer distances
  Hub – multiport repeater (operates on level 1 of the OSI model)
  Switch – receives data from a port, uses packet switching to resolve the destination device and forwards the data to the particular destination (operates on level 2 of the OSI model)

## Slide 52: Bridges and Gateways
Bridge
  Connects two separate but similar Ethernet network segments
  Forwards packets from the source network to the destined network (operates on level 2 of OSI)
Gateway
  Connects networks that work upon different protocols
  The entry and the exit point of a network (controls the access to other networks)
  Level 4, 5, 6 or 7 of the OSI model (same as Firewalls)

## Slide 53: Network Interface Cards – NIC
NIC – a computer component that connects it to the network
There are two types of network cards:
  Internal
  External

## Slide 54: The Future of the Internet

## Slide 55: The Future of the Internet
  A typical modern home consists of: PC, Laptop, Tablet, Phones, TV, Security Camera, Air Conditioner, Smart Watch, Printer, Music Player, Light, etc.
  The "Internet of Things" will expand
    Healthcare, agriculture, wearables, manufacturing
    Smart homes, cars and cities (pollution, parking, energy)
    In 2030 there will be 50 billion devices connected to the Internet of Things

## Slide 56: Summary
…
…
…
Internet, Definitions of Internet
Sending and Receiving Information
OSI model
  Layers
Network Hardware
The Future of the Internet

## Slide 57: Questions?
Notes: 57

## Slide 58: Trainings @ Software University (SoftUni)
Software University – High-Quality Education, Profession and Job for Software Developers
  softuni.bg, about.softuni.bg
Software University Foundation
  softuni.foundation
Software University @ Facebook
  facebook.com/SoftwareUniversity
Software University Forums
  forum.softuni.bg
Notes: 58

## Slide 59: License
This course (slides, examples, demos, exercises, homework, documents, videos and other assets) is copyrighted content
Unauthorized copy, reproduction or use is illegal
© SoftUni – https://about.softuni.bg/
© Software University – https://softuni.bg
Notes: 59